## Slide 1
SEG
MEN
TED
TU
RNI
NG
BALTIMORE AREA TURNERS
November 2016
Ron Ford
Don Keefer

## Slide 2: Segmented turning
“No one in their right mind does segmented turning”

## Slide 3: Why do Segmented Turning?
How does it compare to turning a log ?
Why do segmented turning ?
  Allows for greater creativity
  Use up small pieces
  Much less waste
  Combine multiple species of wood
  No end grain turning
  Can take many forms
    Bowls, lidded vessels, urns, etc

## Slide 4: What tools are required?
Table saw / Miter saw / Bandsaw
Sander
  Belt or Disc (with jig)
Accurate protractor / miter gauge
Thickness sander (optional)
Table saw sled (optional)
Lathe

## Slide 5
It is made from a stack of rings
Rings built from segments
Terminology
  Segment
    Thickness
    Length
    Width
    Miter angle

## Slide 6: PLANNING, PLANNING, PLANNING….
Draw layout with CAD software like SketchUp
(American Woodturner 31: Aug 16)
or…

## Slide 7: PLANNING, PLANNING, PLANNING….
Draw layout on graph paper

## Slide 8: PLANNING, PLANNING, PLANNING….
Draw layout on graph paper

## Slide 9: PLANNING, PLANNING, PLANNING….
Plan the number, the thickness, and species of each ring
How many rings? [rings A thru S] (19)
1. Determine max diameter of each ring
A
S
G
Draw layout on graph paper

## Slide 10: PLANNING, PLANNING, PLANNING….
1. Determine max diameter of each ring
2. Calculate circumference of each ring
  = Diameter x 3.14
3. Decide on number of segments per ring *
  4 or 8 or 12 or 16 or…
A
S
*
*

## Slide 11: PLANNING, PLANNING, PLANNING….
4. Calculate length of each segment
  = Circumference / # of segments

## Slide 12: PLANNING, PLANNING, PLANNING….
5. Calculate miter angle of each segment
  Miter angle = 360o / # of segments /2
  eg. 360o / 16 segments / 2 = 11.25o

## Slide 13: PLANNING, PLANNING, PLANNING….
6. Determine width of each segment/ring
    What affects width?
7. Include a feature ring?
  Design the details of the ring

## Slide 14: PLANNING, PLANNING, PLANNING….
Or, in lieu of calculating it all….

## Slide 15: The Basics
Cut strips on table saw
Length and width of each strip is determined by your calculations
There is more than one way to skin a cat – or to make a segmented turning

## Slide 16: The Basics
Cutting, cutting, cutting….
Use a miter gauge to cut segments
Choose correct angle and length for each segment
Flip strip between each cut … or not…..

## Slide 17: The Basics
The base?
Attach waste block to faceplate
Glue base onto waste block
Several design possibilities for the base:
- One solid piece
- Segmented
- Tapered Plug or
- Floating disc

## Slide 18: The Basics
After cutting the segments - sand them on disc sander

## Slide 19: The Basics
Remove sanding fuzz
Re-sand if necessary
Measure length

## Slide 20: The Basics
No matter how precise you’ve been….
Therefore….

## Slide 21: The Basics
Gluing segments
All at once or…
Each half at once or…
Allen

## Slide 22: The Basics
Gluing segments
Two ** at a time
Tibbetts

## Slide 23: The Basics
Gluing segments

## Slide 24: The Basics
Assembling the rings…
Flatten face of each ring

## Slide 25: The Basics
Assembling…
Glue rings together

## Slide 26: The Basics
Assembling…
Flattening… gluing… flattening… gluing….
flattening.…
gluing…

## Slide 27: The Basics
Assembling & finishing
Final steps

## Slide 28: The icing on the cake: A feature ring OR OTHER EMBELLISHMENT
(Optional)
Plain

## Slide 29: The icing on the cake: A feature ring OR OTHER EMBELLISHMENT
A simple band
(Optional)

## Slide 30: The icing on the cake: A feature ring
A Greek Key

## Slide 31: The icing on the cake: A feature ring
Greek Key
Orientation of grain can be important

## Slide 32: The icing on the cake: A feature ring
Greek Key

## Slide 33: The icing on the cake: A feature ring
Greek Key +

## Slide 34: A feature ring or other embellishments

## Slide 35: The icing on the cake:

## Slide 36: the feature ring or other embellishments

## Slide 37: And Other variations…
Open segments

## Slide 38: And Other variations…
Keep it simple…

## Slide 39: Conclusion
“No one in their right mind does segmented turning”
But who cares! It can be very rewarding….